## Slide 1: B.TECH PROJECT PHASE 1 FIRST REVIEW
SAINTGITS
COLLEGE OF ENGINEERING
(AUTONOMOUS)
LEARN . GROW . EXCEL

## Slide 2: Embodied Semantic Asset Recall Robot Offline Industrial Object Search, Recall, and Verification via Edge-Optimized Vision-Language Models
SAINTGITS
COLLEGE OF ENGINEERING
(AUTONOMOUS)
LEARN . GROW . EXCEL
PRESENTED BY:
Sidharth Sajith
Nidhi N
Tharun Oommen Jacob
Jibin C Basil
SUPERVISOR:
Chinn Mohanan
Assistant Professor
Department of Electronics Engineering
PROJECT AREA : Edge AI, Embedded Systems, Mobile Robotics

## Slide 3
LEARN . GROW . EXCEL
PROBLEM STATEMENT
In shared laboratory and workshop environments, tools, components, and safety equipment are used by multiple people and frequently misplaced. A multimeter borrowed from the electronics bench appears days later on a mechanical shelf; safety goggles vanish before an inspection; a soldering iron moves between workstations without a trace.
Traditional solutions fall short:
• CCTV systems record video but cannot answer spatial queries such as "Where is the multimeter right now?"
• RFID/Barcode systems require tagging every individual item and maintaining reader infrastructure — discipline that rarely survives a busy academic semester
• Manual inventory checks are infrequent, labour-intensive, and error-prone
• Commercial inspection robots (e.g., Boston Dynamics Spot) cost upwards of $75,000, depend on cloud connectivity, and are designed for fixed-infrastructure inspection rather than movable asset recall
This project addresses the gap by developing an autonomous mobile robot that operates fully offline on low-cost edge hardware, builds a persistent semantic memory of objects in a laboratory or workshop, recalls where assets were last seen, navigates to verify their presence, and when an object has been moved, performs probabilistic active search to locate it efficiently.

## Slide 4
LEARN . GROW . EXCEL
TOPIC IDENTIFICATION
• Combines Edge AI, Embedded Systems, and Mobile Robotics
• Relevant to industrial automation, lab/workshop management, and safety compliance
• Provides scope for simulation (Gazebo/Isaac Sim) as well as real-world hardware deployment
• Persistent semantic memory enables queryable spatial knowledge across reboots
• Probabilistic active search for moved objects using Bayesian belief over discrete zones
• Natural-language interaction (voice/text) for intuitive asset recall
• NVIDIA Jetson Orin Nano 8 GB provides suitable edge compute for offline VLM inference
• Smartphone ARCore replaces expensive LiDAR for visual-inertial odometry
• Multi-modal HRI: display for visual feedback, speaker for TTS, microphone array for STT, ultrasonic sensors for close-range obstacle avoidance

## Slide 5
LEARN . GROW . EXCEL
OBJECTIVES
1. Build a reliable mobile base with fused localisation (ARCore VIO + wheel odometry + EKF) achieving ≤0.1 m pose accuracy in a 5 m × 5 m room
2. Develop a two-stage perception pipeline: fast open-vocabulary detection (YOLO-World) running continuously at 5-10 Hz, with event-triggered VLM verification (Florence-2/NanoLLaVA) at keyframes — all on Jetson Orin Nano 8 GB
3. Implement a persistent semantic scene graph (JSON-backed) storing for each asset: unique ID, class, 3D position, timestamp, confidence, spatial relationships (on/inside/near), and carrier associations — surviving power cycles
4. Enable natural-language asset recall: voice/text query → parse intent → navigate to last-known location → visually verify → report with bounding box on display + TTS confirmation

## Slide 6
LEARN . GROW . EXCEL
OBJECTIVES (Contd.)
5. Implement Bayesian active search for moved/missing objects: maintain probability over discrete candidate zones; update beliefs using history priors, semantic priors, carrier relationships, and detection-failure-aware updates
6. Demonstrate three scenarios in a real lab/workshop (internet disabled):
• Stationary tool recall ("Find the multimeter")
• Moved-object search (object secretly relocated → robot reasons, searches, finds)
• Safety compliance inspection ("Check safety items" → patrols → reports present/missing with last-seen locations)
7. Quantify performance against four baselines (random, nearest-zone, last-known-only, semantic-prior) using: success rate, time-to-find, path length, viewpoints visited, edge runtime metrics (RAM, FPS, latency)
8. Multi-modal HRI: 7" touchscreen for object memory cards & heatmap, speaker for TTS responses, 4-mic array for far-field STT, 4× ultrasonic sensors for close-proximity obstacle avoidance supplementing OctoMap

## Slide 7
LEARN . GROW . EXCEL
METHODOLOGY
Literature Survey & Problem Formulation
Study existing semantic mapping, scene graph, probabilistic search, and edge AI methods. Define the offline asset recall problem with constraints (8 GB Jetson, no LiDAR, no cloud).
Hardware & Software Platform Development
Fabricate 4WD chassis with ESP32 motor control. Set up Jetson Orin Nano with JetPack 6, ROS 2 Humble. Develop Android ARCore bridge for VIO + RGB streaming via USB. Integrate micro-ROS on ESP32 for wheel odometry. Additional hardware: 4× ultrasonic sensors (I2C/GPIO) for <0.3m obstacle detection, 7" HDMI touchscreen (800×480), USB speaker, ReSpeaker 4-mic array — all interfaced via Jetson USB/GPIO.
Perception Stack Implementation
Two-stage pipeline: (1) YOLO-World for continuous open-vocabulary detection at 5-10 Hz; (2) Florence-2/NanoLLaVA for verification at keyframes only. Quantize models (AWQ 4-bit) for 8 GB memory budget. Benchmark on curated lab/workshop object dataset.

## Slide 8
LEARN . GROW . EXCEL
METHODOLOGY
Semantic Scene Graph & Persistent Memory
Design object schema (ID, class, position_map, confidence, last_seen, relationships). Implement carrier ontology (on_top_of, inside, beside, near, supported_by). JSON persistence with atomic writes. Query API for recall and search.
Bayesian Search Engine
Discrete zone belief representation. Priors: history (last-seen), gravity, semantic (object class → likely zones), carrier relationships. Updates: detection-failure-aware (reduce, not zero). Priority map generation for next viewpoint selection.
Navigation & Behavior Tree Executive
Stock Nav2 MPPI controller for Phase 2-3. BehaviorTree.CPP trees for: WaitForCommand → ParseIntent → ExecuteSearch (LastKnown → Verify → BayesianSearch loop). Failure handling: nav fail, object not found, multiple matches, VLM unavailable, tracking lost. Ultrasonic fallback: emergency stop / local replanning when OctoMap latency >100ms.
Speech Interface & Dashboard
Whisper.cpp (tiny/base) for offline STT. Piper/Coqui TTS for offline speech synthesis. Intent parser → target class + attributes. React web dashboard + onboard touchscreen: live camera feed, object memory cards, probability heatmap, search reasoning log, replay mode.
Sim-to-Real Validation
Transfer trained/tuned pipeline to physical robot in 5m×5m lab. Evaluate with 10-15 objects, repeated trials. Metrics: SR, time-to-find, path length, viewpoints, edge runtime. Offline demo with Wi-Fi/Bluetooth disabled.

## Slide 9
LEARN . GROW . EXCEL
Research Gap Identified
Existing Research
From thExisting Research (From Literature Survey):
• Semantic mapping extensively studied for robot navigation (VLMaps, ConceptFusion)
• 3D scene graphs with open-vocabulary objects demonstrated (ConceptGraphs, DovSG, HOV-SG)
• Dynamic object tracking via carrier relationships proposed (OpenObject-NAV, DovSG)
• Probabilistic/active search with semantic priors validated (ZAVIS, SEEK, L3MVN)
• Simulation-based training widely used to reduce cost/risk
• Industrial inspection robots prove commercial value (AutoInspect, Spot, Simbe Tally)
• Edge-optimized models enable on-device VLM inference (YOLO-World, Florence-2, NanoLLaVA)

## Slide 10
LEARN . GROW . EXCEL
Research Gap Identified
Identified Gap:
No existing system integrates ALL FIVE of the following:
┌─────────────────────────────────────────────────────────────┐
│ 1. Persistent object-level semantic memory (survives │
│ power cycles, queryable across sessions) │
│ 2. Bayesian active search for moved/missing objects │
│ (belief updates with semantic priors + carrier rels) │
│ 3. Fully offline operation on sub-₹40k robot │
│ 4. Without LiDAR or depth cameras (smartphone ARCore only) │
│ 5. In a real shared lab/workshop environment (not sim) │
└─────────────────────────────────────────────────────────────┘
Specific gap: No work demonstrates a low-cost, fully offline, mobile semantic asset-recall system for small shared workspaces where objects are movable, untagged, and visually identified without cloud AI, RFID, or LiDAR.

## Slide 11
LEARN . GROW . EXCEL
LITERATURE SURVEY
TITLE | ABOUT | REFERENCE
VLMaps | Constructs 3D semantic maps by fusing VLM features into a volumetric or point-based map representation. Enables open-vocabulary navigation by querying the map with natural language without predefined object categories. Uses pre-trained VLMs to embed multi-scale image patches into 3D, supporting zero-shot spatial reasoning and language-guided exploration. | Huang et al., ICRA 2023
ConceptGraphs | Builds open-vocabulary 3D scene graphs where nodes are object instances with CLIP embeddings and edges encode spatial/semantic relationships. Leverages foundation models to detect, segment, and classify objects without closed-set labels. Supports hierarchical scene understanding and enables downstream tasks like language-guided manipulation and task planning through graph queries. | Gu et al., ICRA 2024
DovSG | Addresses long-term robotic operation by maintaining a dynamic 3D scene graph that incrementally updates as the environment changes. Handles object addition/removal, state changes (open/closed), and spatial relocation over weeks/months. Uses change detection on VLM embeddings and geometric consistency checks to fuse new observations while preserving persistent object identities—critical for lifelong learning and continual navigation. | Zhu et al., RA-L 2025

## Slide 12
LEARN . GROW . EXCEL
LITERATURE SURVEY(Contd…)
TITLE | ABOUT | REFERENCE
SEEK | Proposes a semantic reasoning framework for object search that combines LLMs with scene graphs. The LLM generates search hypotheses (e.g., "mugs are usually in kitchens") which are grounded in a 3D scene graph to plan efficient exploration trajectories. Integrates commonsense reasoning with geometric mapping to reduce search time in unfamiliar environments. | Ginting et al., RSS 2024
Open Scene Graphs | Introduces a persistent, open-vocabulary 3D scene graph as long-term semantic memory for navigation. Unlike episodic maps, it accumulates knowledge across multiple deployments, merging observations via VLM-based place recognition and object re-identification. Supports queries and enables zero-shot navigation to semantically specified goals across sessions. | Loo et al., IJRR 2024
YOLO-World / Florence-2 | YOLO-World: Real-time open-vocabulary detection using vision-language pre-training; accepts text prompts at inference to detect arbitrary classes without retraining. Florence-2: Unified vision foundation model handling detection, segmentation, captioning, and grounding via a single transformer with task prompts. Both provide the perception backbone for modern robotics, enabling vision and thought capabilities for semantic mapping and reasoning. | Cheng et al., CVPR 2024 / Xiao et al., 2023

## Slide 13
Proposed Project Focus
The proposed work focuses on developing an offline semantic asset recall system for a low-cost mobile robot, training and evaluating it in a real laboratory/workshop environment, with persistent memory, probabilistic moved-object search, and natural-language interaction — all running on Jetson Orin Nano 8 GB without cloud dependency.
PROJECT CONTRIBUTIONS
1. Low-Cost Offline Architecture: Complete mobile robot (₹35k-40k) with smartphone ARCore VIO replacing LiDAR, running full perception-navigation-memory-search pipeline on Jetson Orin Nano 8 GB
2. Persistent Semantic Scene Graph: JSON-backed object-level memory storing identity, 3D location, timestamp, confidence, spatial relationships (on/inside/near), and carrier associations — surviving reboots
3. Two-Stage Edge Perception Pipeline: YOLO-World (continuous, 5-10 Hz) + Florence-2/NanoLLaVA (event-triggered verification) with AWQ 4-bit quantization, scheduled via keyframe policy to fit 8 GB RAM
4. Bayesian Active Search Engine: Discrete-zone belief with history, semantic, carrier, and gravity priors; detection-failure-aware updates; priority map for viewpoint selection; explainable reasoning log
5. Multi-Modal Human-Robot Interface: Onboard 7" touchscreen (object cards, heatmap), speaker (TTS responses), 4-mic array (far-field STT), ultrasonic ring (close-proximity safety) — all offline
6. End-to-End Real-World Validation: Three demonstrated scenarios (stationary recall, moved-object search, safety inspection) with quantitative comparison against 4 baselines; offline demo with internet disabled; 15+ min continuous operation

## Slide 14
LEARN . GROW . EXCEL
ROAD MAP
Not completed
Partially completed
Fully completed

## Slide 15
LEARN . GROW . EXCEL
RESOURCE REQUIREMENTS
SOFTWARE REQUIREMENTS
• NVIDIA JetPack 6 / Ubuntu 22.04 — Base OS for Jetson Orin Nano
• ROS 2 Humble Hawksbill — Robotics middleware, Nav2, TF2, robot_localization
• NVIDIA Isaac Sim / Isaac Lab — Simulation environment for pre-deployment testing
• Gazebo (Harmonic/Igloo) — Alternative simulation with ROS 2 integration
• Python 3.10+ — RL/perception implementation, scripting
• PyTorch / ONNX Runtime — Model inference on Jetson (TensorRT optimization)
• YOLO-World (AILab-CVC) — Open-vocabulary object detection
• Florence-2 / NanoLLaVA — Vision-language model for verification
• Whisper.cpp (ggml) — Offline speech-to-text (tiny/base model)
• Piper / Coqui TTS — Offline text-to-speech (lightweight, multi-speaker)
• BehaviorTree.CPP + Groot2 — Behavior tree executive & visualization
• OctoMap — 3D occupancy mapping (5 cm voxel resolution)
• React / TypeScript — Web dashboard (object cards, heatmap, replay)
• Android Studio + ARCore SDK — Smartphone VIO bridge application
• micro-ROS (ESP-IDF) — ESP32 firmware for motor control + odometry
• Git + GitHub/GitLab — Version control, CI/CD, issue tracking

## Slide 16
LEARN . GROW . EXCEL
RESOURCE REQUIREMENTS
HARDWARE REQUIREMENTS
COMPUTE & SENSING
• NVIDIA Jetson Orin Nano 8 GB Developer Kit — Main compute
• ARCore-compatible Android smartphone — VIO + RGB camera (already owned)
• ESP32 DevKit — Motor control, wheel encoders, micro-ROS
MOBILITY & POWER
• 3D printed chassis with encoder motors — Differential drive base
• BO/GB37 geared motors with quadrature encoders (4×)
• Motor driver BTS7960 (2×) — High-current dual H-bridge
• 4S LiPo battery (14.8V, 5000 mAh, 50C) + balance charger
• 5V/8-10A buck converter (Jetson) + 5V logic regulator (ESP32/sensors)
• Powered USB 3.0 hub (7-port) — Phone + ESP32 + mic + peripherals
PERCEPTION & HRI
• 4× Ultrasonic sensors (HC-SR04 / JSN-SR04T) — Near-field obstacle avoidance
• 7" HDMI Touchscreen (800×480, IPS) — Onboard display for object cards/heatmap
• USB Speaker (5W+) — TTS audio output
• ReSpeaker 4-Mic Array (USB) — Far-field STT, beamforming

## Slide 17
LEARN . GROW . EXCEL
RESOURCE REQUIREMENTS
HARDWARE REQUIREMENTS
MISCELLANEOUS
• Wheels (80-100mm) + castor
• Wiring, connectors, fuses, switches, XT60, JST
• 3D printing (mounts, brackets, sensor housings, covers)
• Lab test objects (10-15 classes): multimeter, soldering iron, screwdriver, pliers, tape, ESP32 board, motor driver, battery pack, safety goggles, helmet, first-aid kit, toolbox, extension board, project box

## Slide 18
LEARN . GROW . EXCEL
TASK ALLOCATION
Task 1 – Literature Survey, Problem Formulation & Architecture Design
• Detailed literature survey across 5 research areas (25+ papers)
• Study edge AI models (YOLO-World, Florence-2, NanoLLaVA, Whisper.cpp, Piper TTS)
• Define system architecture: 9-layer stack (Mobility → Interface)
• Edge vs Cloud trade-off analysis for architectural decision
• Identify research gap & finalize project contributions
Task 2 – Hardware Fabrication & Low-Level Control
• Chassis fabrication (3D printed / metal), motor mounting, wiring
• ESP32 firmware: micro-ROS, encoder reading, PID velocity control
• Power system: battery management, buck converters, fusing, voltage monitoring
• Phone mount design: rigid, vibration-damped, calibrated extrinsics
• Ultrasonic sensor ring: PCB design, GPIO/I2C interfacing, ROS 2 driver
• Physical workspace setup: 5m×5m lab with bench, shelf, tool zones
Task 3 – Software Platform & Data Pipeline
• Jetson flash, JetPack 6, ROS 2 Humble workspace setup
• Android ARCore bridge: pose + RGB + IMU → ROS 2 topics (/tf, /camera/image_raw)
• USB throughput optimization, timestamp synchronization
• robot_localization EKF: fuse ARCore VIO + wheel odometry + IMU
• OctoMap mapping pipeline, RViz visualization (map, TF, heatmap)
• Ultrasonic driver: ROS 2 node publishing /ultrasonic/range array, fused in costmap

## Slide 19
LEARN . GROW . EXCEL
TASK ALLOCATION
Task 4 – Perception Stack & Semantic Memory
• Model benchmarking on PC → Jetson (latency, memory, accuracy on lab objects)
• AWQ 4-bit quantization, TensorRT optimization for 8 GB budget
• Two-stage pipeline: YOLO-World (continuous) + VLM (keyframe-triggered)
• Semantic scene graph: JSON schema, persistence, carrier ontology, query API
• Object memory cards: ID, class, position, confidence, relationships, last_seen
Task 5 – Bayesian Search, Navigation & Behavior Tree
• Discrete zone belief representation, prior formulation (history, semantic, carrier, gravity)
• Detection-failure-aware Bayesian update, priority map generation
• Nav2 MPPI configuration, costmap, parameter tuning
• Ultrasonic integration in local costmap for emergency stop / replanning
• BehaviorTree.CPP: WaitForCommand → ParseIntent → ExecuteSearch (fallback tree)
• Failure states: nav fail, not found, multiple matches, VLM unavailable, tracking lost
• VisualCoverageCritic prototype (Phase 3+)
Task 6 – Speech Interface, Display, Dashboard & System Integration
• Whisper.cpp (tiny/base) STT + Piper TTS integration, push-to-talk → intent parser
• 7" touchscreen GUI: object memory cards, probability heatmap, search log, system status
• React web dashboard (mirror): live camera, object cards, heatmap, search replay
• End-to-end integration testing, 15-min stress runs, RAM/CPU profiling
• Offline validation (Wi-Fi/Bluetooth disabled), three demo scenarios
• Final report, paper draft, viva preparation

## Slide 20
LEARN . GROW . EXCEL
TASK ALLOCATION
Task 7 – Documentation, Reporting & Project Management
• Weekly progress logs, Git commits, architecture decision records (docs/decisions/)
• Phase reports (4 phases), First Review PPT, Final Report, Paper manuscript
• Budget tracking, procurement logs, risk register updates

## Slide 21
LEARN . GROW . EXCEL
REFERENCES
[1] C. Huang, O. Mees, A. Zeng, and W. Burgard, "Visual Language Maps for Robot Navigation," Proc. IEEE ICRA, London, UK, pp. 10608-10615, 2023.
[2] K. Jatavallabhula et al., "CLIP-Fields: Weakly Supervised Semantic Fields for Robotic Memory," Proc. RSS, 2022.
[3] K. Jatavallabhula et al., "ConceptFusion: Open-Set Multimodal 3D Mapping," Proc. RSS, 2023.
[4] Q. Gu et al., "ConceptGraphs: Open-Vocabulary 3D Scene Graphs for Perception and Planning," Proc. IEEE ICRA, 2024.
[5] Z. Yan et al., "Dynamic Open-Vocabulary 3D Scene Graphs for Long-Term Language-Guided Mobile Manipulation (DovSG)," IEEE RA-L, 2025.
[6] J. Loo et al., "Open Scene Graphs for Open-World Object-Goal Navigation," 2024.
[7] X. Li et al., "OpenObject-NAV: Open-Vocabulary Object-Oriented Navigation Using Dynamic Carrier-Relationship Scene Graphs," arXiv:2409.18743, 2024.
[8] X. Li et al., "OpenIN: Open-Vocabulary Instance-Oriented Navigation in Dynamic Environments," arXiv:2501.04279, 2025.
[9] M. Karnan et al., "ZAVIS: Zero-Shot Active Visual Search," arXiv:2209.08803, 2022.
[10] M. Ginting et al., "SEEK: Semantic Reasoning for Object Goal Navigation in Real-World Inspection Tasks," Proc. RSS, 2024.

## Slide 22
LEARN . GROW . EXCEL
THANKYOU